## Slide 1: Mold Prevention System
Internet of Things
05.02.2025
by:
Jonas Ohmaescher

## Slide 2: Contents 1. Introduction 2. Analysis 3. Design 4. Prototype 5. Conclusion

## Slide 3: 1. Introduction
Goals of the Project
Develop an IoT system
  Monitor environmental data
  Supports the user to create a good living environment
  Prevent Mold
    crucial in houses with bad ventilation or during cold seasons
How does Mold develop?
High indoor humidity (>60%)
  creates moisture
Poor ventilation
Warmth

## Slide 4: 1. Introduction
Relative Humidity vs. Absolute Humidity
Relative Humidity:
Descibes how humid the air feels
Absolute Humidity:
Amount of Water per cubic meter

## Slide 5: 2. Analysis
Competitors
Mi Temperature and Humidity Monitor 2
made by Xiaomi
offers Bluetooth connection
  also to other devices (Heating, etc…)
Smart Home Hub 2 for User Notification
Room thermostat II
made by Bosch Smart Home
works similar to the one made by Xiaomi
devices have Bluetooth connection
Controller offers access trough the internet
Costs: 10€
+ 35€ for Ground Station
Costs: 80€
+ 100€ for Controller

## Slide 6: 2. Analysis
Functional Requirements
ID | Requirement | Input | Output
FR1 | Indoor Temperature and Humidity Monitoring | Current room temperature and humidity | System status update
FR2 | Outdoor Temperature and Humidity Monitoring | Current outdoor temperature and humidity at a specific location | System status update
FR3 | Absolute Humidity Calculation | Temperature and Relative Humidity | System status update
FR4 | Compare Indoor and Outdoor Absolute Humidity | Absolute Humidity | System status update, Flag
FR5 | User Notification to recommend when the window should be opened | Absolute Humidity Comparison | Notification to the user
FR6 | User Warning for high indoor Relative Humidity | Indoor Relative Humidity | Alert notification to the user
FR7 | Update Sensor Configuration | Sensor Configuration Data | Updated System
FR8 | Update Thresholds | User Input | Updated System
FR9 | User Registration | User data | Registered User
FR10 | House Registration | House data | Updated System
FR11 | Remote Window Opening | User command | Window opened, or ventilation system started

## Slide 7: 2. Analysis
Non-Functional Requirements
NFR1 - Cost-Effectiveness The system must be affordable to ensure accessibility for a broad range of users.
NFR2 - Energy Efficiency Sensors must operate with low power consumption to ensure extended battery life. Data transmission must be optimized to reduce energy usage.
NFR3 – Real Time Notifications The system must send real-time notifications to users about updates or issues, ensuring timely actions.
NFR4 - Environmental Conditions Indoor sensors must operate reliably within 0°C to 50°C and 10%-90% Humidity. Outdoor sensors must operate reliably within -20°C to 50°C and 0%-100% Humidity. Outdoor sensors must withstand environmental conditions such as rain, frost, and heat.

## Slide 8: 2. Analysis
Hardware Choices
Temperature and Humidity Sensor
DHT11
  cheapest one
  measuring range doesn´t fulfill outdoor requirements
  DHT22
    Fulfill requirements
    good accuracy

## Slide 9: 2. Analysis
Hardware Choices
Boards
NodeMCU is chosen
cheapest one
fulfills the requirements
offers all the needed connectivity

## Slide 10: 2. Analysis
Hardware Choices
Remote Window Opening
NodeMCU Relay Module is chosen
Actuators could be connected to the Relay

## Slide 11: 2. Analysis
Communication
MQTT is selected

## Slide 12: 3. Design
Overview

## Slide 13: 3. Design
Overview
├── Application Layer (Interface & APIs)
│
├── Digital Twin Layer (Core Logic)
│
├── Services Layer (Business Logic)
│
└── Virtualization Layer (Digital Replicas)

## Slide 14: 3. Design
Virtualization Layer

## Slide 15: 3. Design
Services Layer
Fetch Weather Service
Open-Meteo
  open source weather API
  free and easy to use
  Input: Longitude and Latitude
returns current temperature and humidity
Humidity Comparison Service
compares Absolute Humidity
  Room
  House
returns Absolute Humidity difference
User Notification Service
sends a notification to a logged user trough telegram
Input is the user_id and the text message

## Slide 16: 3. Design
Digital Twin Layer
HouseFactory(DTFactory)
HouseTwin(DigitalTwin)
Function Name | Description
add_room | Adds a Room reference to a Digital Twin
remove_room | Removes a Room reference from a Digital Twin
update_temperature_humidity | Updates temperature and humidity values for a Digital Twin.
Function Name | Description
add_longitude | Adds longitude attribute
add_latitude | Adds latitude attribute
add_temperature | Adds temperature attribute
add_relative_humidity | Adds relative humidity attribute
calculate_absolute _humidity | Calculates and sets absolute humidity based on temperature and relative humidity
add_rooms | Adds rooms attribute

## Slide 17: 3. Design
Application Layer
Database APIs
Function name | Route | HTTP Method | Description
create_house | /api/house/ | POST | Creates a new house digital replica.
get_house | /api/house/<house_id> | GET | Retrieves details of a specific house.
list_houses | /api/house/ | GET | Lists all houses with optional filtering.
create_room | /api/house/<house_id> /rooms | POST | Creates a new room within connected to a house.
get_room | /api/house/<house_id> /rooms/<room_id> | GET | Retrieves details of a specific room.
create_device | /api/ventilation/ | POST | Creates a new ventilation digital replica.
get_device | /api/ventilation /<ventilation_id> | GET | Retrieves details of a specific ventilation device.
list_devices | /api/ventilation/ | GET | Lists all ventilation devices with optional filtering.
toggle_ventilation | /api/ventilation /<ventilation_id>/toggle | POST | Toggles the state of a specific ventilation device between on and off.
create_device | /api/ventilation/ | POST | Creates a new ventilation digital replica.
register_user | /api/user/register | POST | Registers a new user.
list_rooms | /api/user/<user_id> /rooms | GET | Lists all rooms connected to a specific user.
assign_user | /api/user/<user_id> /assign/<room_id> | POST | Assigns a room to a specific user.

## Slide 18: 3. Design
Application Layer
Telegram APIs
Function Name | Command | Description
login_handler | /login <username> <password | User login with credentials. List assigned rooms to the user.
logout_handler | /logout | User logout
list_rooms | /list_rooms | List all the rooms assigned to the user
get_room_status | /status | Handler to get the status of all rooms assigned to the user
ventilation_on_handler | /ON <ventilation_id> | Switches on <ventilation_id> Device
ventilation_off_handler | /OFF <ventilation_id> | Switches off <ventilation_id> Device

## Slide 19: 3. Design
Application Layer
Telegram APIs
Example using /status

## Slide 20: 3. Design
Application Layer
MQTT Measurement Handler
Running on the Flask Server
Subsciber
handles incoming messages in the measurement topic

## Slide 21: 3. Design
Application Layer
MQTT Ventilation Handler
Running on the Flask Server
Publisher
sends messages to the ventilation topic

## Slide 22: 4. Prototype
Measurement Device
used DHT11 instead of the DHT22
setup of the mqtt broker was complicated
sends measured data to the measurement topic

## Slide 23: 4. Prototype
Ventilation Device

## Slide 24: 5. Conclusion
ID | Requirement | Input | Output | Fulfilled
FR1 | Indoor Temperature and Humidity Monitoring | Current room temperature and humidity | System status update | yes
FR2 | Outdoor Temperature and Humidity Monitoring | Current outdoor temperature and humidity at a specific location | System status update | (yes)
FR3 | Absolute Humidity Calculation | Temperature and Relative Humidity | System status update | yes
FR4 | Compare Indoor and Outdoor Absolute Humidity | Absolute Humidity | System status update, Flag | yes
FR5 | User Notification to recommend when the window should be opened | Absolute Humidity Comparison | Notification to the user | yes
FR6 | User Warning for high indoor Relative Humidity | Indoor Relative Humidity | Alert notification to the user | yes
FR7 | Update Sensor Configuration | Sensor Configuration Data | Updated System | no
FR8 | Update Thresholds | User Input | Updated System | no
FR9 | User Registration | User data | Registered User | (yes)
FR10 | House Registration | House data | Updated System | (yes)
FR11 | Remote Window Opening | User command | Window opened, or ventilation system started | yes

## Slide 25: Thanks a lot for your attention!
Questions?